## Slide 1
SEAtS | 264726
Introduction to Systematic
Design of Multi-
Component Systems

## Slide 2
By the end of this lecture, you will be able to:
Identify the diﬀerences between monolithic and distributed design
approaches.
Describe the key principles of a systematic design process.
Explain the importance of interfaces and coordination in distributed
system development.
Evaluate tools and methods used to support the systematic design of
complex systems.
Apply a systematic design process to a simpliﬁed real-world
engineering problem.
Intended
Learning
Outcomes
SEAtS | 264726
Version: 19d8ced | © 05.10.2026 University of Southampton
2

## Slide 3
Modern products and systems are increasingly complex and interconnected, demanding robust, adaptable
and Scalable designs; ad hoc approaches inherently increase risk.
SEAtS | 264726
Problem statement
Version: 19d8ced | © 05.10.2026 University of Southampton
3

## Slide 4
Designing modern engineering systems often involves combining
mechanical, electrical, and software components, each with its own
functional logic and physical constraints.
A robot, for example, may contain a motion controller, sensors,
actuators, communication links, and onboard processing. Such systems
cannot be designed eﬀectively without breaking the problem down,
coordinating sub-systems, and validating their integration.
Modern engineering components
SEAtS | 264726
Modern Engineering
Version: 19d8ced | © 05.10.2026 University of Southampton
4

## Slide 5
Recall from the Systems Thinking lecture: systemic design accounts for the whole system and its feedback
loops; systematic design breaks it into orderly, methodical steps. This lecture goes deep on the second.
SEAtS | 264726
Recap: Systemic vs. Systematic
Design
Version: 19d8ced | © 05.10.2026 University of Southampton
5

## Slide 6
Systemic Design
A design approach that integrates systems thinking into the design process to address
complex, interconnected, socio-technical challenges involving multiple stakeholders and
dynamic relationships.
Key characteristics:
Emphasises relationships, feedback loops, and emergent behaviours
Integrates qualitative and quantitative analysis
Focused on sense-making and co-creation in messy, real-world contexts
Often applied to sustainability, healthcare, policy, education, and ecosystems
DEFINITION
SEAtS | 264726
Version: 19d8ced | © 05.10.2026 University of Southampton
6

## Slide 7
Systemic Design Principles
A common systemic design mindset includes:
Acknowledging interconnections
Redeﬁning waste as a resource
Designing self-organising systems
Using feedback as a guide to adaptive improvement
These mindsets are increasingly important as engineers face challenges that are not purely
technical but socio-technical, requiring both human and machine systems to work
harmoniously.
DEFINITION
SEAtS | 264726
Version: 19d8ced | © 05.10.2026 University of Southampton
7

## Slide 8
Worked Example: Redesigning a Recommender
System
Where [[systems-thinking]]
diagnoses
the algorithm/user feedback loop that produces ﬁlter
bubbles (see [[social-media-algorithm-feedback]]), systemic design
redesigns the whole
system
, not just the algorithm:
Change recommendation weights to penalise extreme content
Redesign the UI to surface opposing viewpoints and trigger reﬂection
Change creator incentives from engagement-maximisation to quality
Add circuit breakers that inject diverse content when a feed becomes too homogeneous
Monitor for emergent polarisation across the whole platform
These interventions only work
together
: changing the algorithm without changing incentives
still lets creators game the system; showing opposing views without changing the algorithm
gets them ignored. Systemic design means designing across the system, not one component
at a time — see [[systematic-design]] for how the same scenario looks run as a phased
process instead.
DEFINITION
SEAtS | 264726
Version: 19d8ced | © 05.10.2026 University of Southampton
8

## Slide 9
Systematic Design
Systematic Design is a structured approach that decomposes systems into interacting
components, applying design principles to manage intricate challenges eﬀectively.
1.
Structured: Following repeatable processes with deﬁned stages and checkpoints rather
than intuitive approaches. This ensures consistency and quality across projects.
2.
Decomposable: Breaking complex problems into manageable sub-problems that can be
addressed independently, while maintaining awareness of interactions.
3.
Iterative: Embracing feedback loops to continuously reﬁne designs based on testing,
simulation, and stakeholder input throughout the development lifecycle.
Systematic design is crucial for managing complexity, coordinating distributed teams, and
ensuring that each subsystem contributes eﬀectively to the global performance objectives. It is
not simply a way to document a design process.
DEFINITION
SEAtS | 264726
Version: 19d8ced | © 05.10.2026 University of Southampton
9

## Slide 10
Is about rigour and discipline in the design workﬂow
It stands in contrast to systemic design and systems thinking, which emphasise
interconnections, feedback loops, and emergent behaviour in messy, socio-technical contexts
rather than phased rigour, and to ad hoc design approaches, which rely on designer intuition
and past experience without structured methodologies.
In multi-component systems, systematic design becomes essential because complexity grows
exponentially with each additional component, and it draws on the practical toolkit captured in
"Systematic Design Principles" and the monolithic vs distributed design choice for how the
resulting process is coordinated.
Where systematic design is process-oriented and phased, systemic design is relationship-
oriented and participatory, making it the bridge between systems thinking (the analytical lens)
and the structured discipline of systematic design (the delivery process).
It is a foundational approach that ensures:
1. Reliability
2. Scalability
3. Integration
are establisahed across subsystems when applied to multi-component systems. It integrates
DEFINITION
SEAtS | 264726
Version: 19d8ced | © 05.10.2026 University of Southampton
10

## Slide 11
Key Principles of Systematic Design
Principle
Description
Structured Process Orientation
Follow a deﬁned, repeatable sequence of design stages to ensure
clarity and consistency.
Problem Decomposition
Break the system into manageable subsystems or components to
reduce complexity.
Function-Driven Design
Begin with the desired functions and derive solutions that fulﬁll
those functions.
Design Space Exploration and
Evaluation
Generate multiple design alternatives and evaluate them using
clear, objective criteria.
Interface Deﬁnition and
Integration Planning
Clearly deﬁne interfaces between components to ensure
compatibility and successful integration.
Requirements Traceability
Link every design decision back to a functional or non-functional
requirement.
DEFINITION
SEAtS | 264726
Version: 19d8ced | © 05.10.2026 University of Southampton
11

## Slide 12
Worked Example: A Systematic Redesign Process
Continuing the same scenario as [[systemic-design]]'s worked example, a systematic approach
to redesigning a recommender system looks like an ordered checklist:
1. Audit the current recommendation algorithm
2. Design a new weighting scheme
3. Build A/B test infrastructure
4. Run tests on 10% of users
5. Measure engagement metrics
6. Roll out to 100% if metrics improve
Each step is methodical and auditable — but, taken alone, isolated: step 1 doesn't show how it
aﬀects step 4, or how improving one metric breaks another part of the system. That's the gap
[[systemic-design]] closes.
DEFINITION
SEAtS | 264726
Version: 19d8ced | © 05.10.2026 University of Southampton
12

## Slide 13
SEAtS | 264726
Question
Version: 19d8ced | © 05.10.2026 University of Southampton
13

## Slide 14
Its elegance lies in its systematic approach to a singular function. This humble oﬃce tool exempliﬁes
several key principles of systematic design:
SEAtS | 264726
The Elegance of the Paperclip
📎
Securely holds papers together without tearing or
damaging them, fulﬁlling its core purpose ﬂawlessly.
Clear Functionality
Utilises a single, continuous piece of bent wire,
minimising waste and complexity in its construction.
Material Eﬃciency
Its simple form allows for cost-eﬀective mass
production, making it widely accessible and aﬀordable.
Ease of Manufacturing
Recognised and eﬀective worldwide, demonstrating a
timeless and robust design solution for a common
problem.
Universal Adaptability
Version: 19d8ced | © 05.10.2026 University of Southampton
14

## Slide 15
An EV is a highly integrated ecosystem of disparate components, each requiring meticulous design and
seamless coordination. Which hinges on the harmonious interaction of these diverse systems.
SEAtS | 264726
Real-World Complexity: EV
⛐
Integrated electric motors, high-voltage batteries, and
intricate power electronics for propulsion.
Powertrain
Advanced Battery Management Systems, autonomous
driving, and sophisticated infotainment.
Software Systems
Lightweight structures, advanced suspension, and
comprehensive safety features protecting occupants.
Chassis & Safety
Intuitive digital interfaces, connectivity, and intelligent
climate control for passenger comfort.
User Experience
Version: 19d8ced | © 05.10.2026 University of Southampton
15

## Slide 16
SEAtS | 264726
Question
Version: 19d8ced | © 05.10.2026 University of Southampton
16

## Slide 17
The systematic design process can be represented in the following stages:
1. Inquiry – Understand system context, user needs, and constraints
2. Framing & Requirements Gathering – Deﬁne the scope, boundaries, and stakeholder expectations
3. System Architecture & Interface Deﬁnition – Decompose system into components; deﬁne interaction
contracts
4. Component Design & Optimisation – Apply appropriate methods (e.g., FEA, simulation, surrogate
modelling)
5. Integration & Testing – Assemble components, verify performance against system requirements
6. Feedback & Iteration – Use simulation and real-world data to reﬁne models
SEAtS | 264726
Systematic Design Process
Overview
Version: 19d8ced | © 05.10.2026 University of Southampton
17

## Slide 18
To support these phases, engineers and designers use a range of tools:
SEAtS | 264726
Tools Supporting Systematic
Design
1)
Prediction / surrogate
models
2)
Optimization
Algorithms
3)
Simulation and
Validation
4)
System Mapping Tools
5)
Prototyping and Implementation
Version: 19d8ced | © 05.10.2026 University of Southampton
18

## Slide 19
SEAtS | 264726
Question
Version: 19d8ced | © 05.10.2026 University of Southampton
19

## Slide 20
A multi-component system is composed of physically or functionally distinct elements that work together
to deliver a complete functionality. Eﬀective system design requires balancing these elements:
1. System-level requirements that address the overall purpose
2. Component-level speciﬁcations that drive individual elements
3. Interface deﬁnitions that ensure compatibility
Design Drivers
1. Performance metrics (speed, accuracy, eﬃciency)
2. Cost constraints (materials, manufacturing, lifecycle)
3. Modularity requirements (maintenance, upgradeability)
4. Time-to-market pressures
SEAtS | 264726
Understanding Multi-Component
Systems
Version: 19d8ced | © 05.10.2026 University of Southampton
20

## Slide 21
Challenge
Impact
Interface complexity
Integration failures, rework
Cross-disciplinary coordination
Misalignment, communication breakdown
Requirements instability
Design churn, rework
Scalability
Process overhead and design delays
Limited design exploration
Missed innovation opportunities
Tool integration
Ineﬃciencies, data loss
Change propagation
System-wide knock-on eﬀects
Testing bottlenecks
Undetected errors, delayed feedback
Traceability management
High documentation cost
Human factors
Non-compliance, lack of buy-in
SEAtS | 264726
Challenges in Systematic Design
of Multi-Component Systems
Version: 19d8ced | © 05.10.2026 University of Southampton
21

## Slide 22
A key challenge in multi-component systems is managing the interfaces between components. Interfaces
deﬁne how data, energy, or force is exchanged between components and are critical to system
functionality.
This allows each component to be optimized independently, However, such decomposition risks missing
globally optimal solutions or producing physically infeasible designs.
SEAtS | 264726
Interface complexity
In mechanical design, interface
stiﬀness matrices describe how
forces and displacements are
related across component
boundaries.
Mechanical
Design
In software systems, APIs deﬁne
function calls and data structures.
Software
Systems
In embedded systems, protocols
govern timing and synchronization.
Embedded
Systems
Version: 19d8ced | © 05.10.2026 University of Southampton
22

## Slide 23
This shift from global to local design parallels organisational design: individual teams can work on parts as
long as shared protocols and interfaces are respected.
SEAtS | 264726
Monolithic vs Distributed Design
Monolithic design approaches attempt to optimize all
design variables simultaneously in a single, tightly
integrated process. This has the advantage of
potentially achieving globally optimal solutions but
suﬀers from scalability issues and coordination
challenges in practice.
Monolithic design
Distributed design optimization, on the other hand,
decomposes the global design problem into
subproblems, each associated with a component or
subsystem. Coordination is then required to ensure that
the subproblem solutions are compatible and converge
to a system-level optimum.
Distributed design
Version: 19d8ced | © 05.10.2026 University of Southampton
23

## Slide 24
SEAtS | 264726
Question
Version: 19d8ced | © 05.10.2026 University of Southampton
24

## Slide 25
Systemic design integrates systems thinking with design thinking. It shifts from linear workﬂows to
iterative, participatory approaches.
For AI engineers, this means:
Designing not just algorithms, but ecosystems.
Moving beyond optimisation for accuracy towards resilience, fairness, and sustainability.
Using participatory design to include diverse stakeholders, ensuring systems reﬂect real-world needs
and values.
SEAtS | 264726
Systemic Design and AI
Version: 19d8ced | © 05.10.2026 University of Southampton
25

## Slide 26
In engineering, decomposing large systems into sub-components is a common strategy. Distributed design
optimisation methods demonstrate how monolithic systems can be decomposed into manageable
subproblems, coordinated through meta-models and surrogate functions.
For AI:
Training pipelines can be seen as multi-component systems (data preprocessing, model training,
inference, deployment).
Distributed optimisation mirrors federated learning, where subsystems (clients) optimise locally but
must contribute to global system coherence.
Challenges such as coordination overhead and physical feasibility echo AI engineering struggles:
ensuring that independent model updates remain consistent, feasible, and ethical.
SEAtS | 264726
Distributed and Optimised AI
Systems
Version: 19d8ced | © 05.10.2026 University of Southampton
26

## Slide 27
AI-speciﬁc tooling show how systems thinking integrates with day-to-day engineering workﬂows.
(e.g., system dynamics simulators, monitoring dashboards, datasheets/model cards)
Giga-mapping: Large-scale visualisation of system interconnections.
Causal Loop Diagrams: Identifying reinforcing/balancing loops.
Informed Decomposition: Breaking down optimisation tasks into smaller subproblems without
excessive coordination.
Stakeholder Analysis Matrices: Mapping inﬂuence and interests of actors.
SEAtS | 264726
Tools and Methods
Version: 19d8ced | © 05.10.2026 University of Southampton
27

## Slide 28
Is it about keep things cool?
SEAtS | 264726
Case Study
Version: 19d8ced | © 05.10.2026 University of Southampton
28

## Slide 29
Bullet Proof Fridges
built with heavy steel, thick insulation, and very long lifespans (some lasted 40+ years).
SEAtS | 264726
First household electric fridges
became commercially available,
replacing iceboxes.
Introduced sealed refrigerant
systems (using toxic gases at
ﬁrst, later safer ones).
Improved food safety by
slowing spoilage.
1920s, 30's
Mass adoption after WWII, as
manufacturing shifted back to
consumer goods.
More reliable compressors and
safer refrigerants (Freon).
First freezer compartments
introduced for limited frozen
storage.
1940s
Fridges became a staple in
middle-class homes.
Chrome ﬁnishes, rounded
designs, and interior lighting
added.
Larger freezer sections allowed
frozen food markets to grow.
1950s
Version: 19d8ced | © 05.10.2026 University of Southampton
29

## Slide 30
The Cheap Fridges
Slightly lower quailty but designs shifted toward convenience and style (ice makers, side-by-side doors),
which sometimes reduced durability.
SEAtS | 264726
Automatic defrosting (no more
manual ice scraping).
Adjustable shelves and door
storage.
More eﬃcient insulation and
compressors reduced energy
use compared to earlier models.
1960s
Energy crisis led to new
eﬃciency standards.
Introduction of tighter door
seals and improved insulation.
More focus on durability and
safety of refrigerants.
1970s
Side-by-side fridge/freezer
designs became popular.
Ice and water dispensers built
into the door.
Energy-eﬃcient models
introduced due to stricter
regulations.
1980s
Version: 19d8ced | © 05.10.2026 University of Southampton
30

## Slide 31
The Compliance Fridges
more electronics and plastic parts made repairs harder and sometimes reduced lifespan compared to
earlier “bulletproof” models.
SEAtS | 264726
Microprocessor-based controls
for precise temperature
regulation.
Use of CFC-free refrigerants
(environmental shift after
Montreal Protocol).
Better humidity control for fresh
produce.
1990s
Sleeker designs with stainless
steel ﬁnishes.
Multi-zone cooling systems
(diﬀerent temperatures for
diﬀerent compartments).
Introduction of energy ratings
and eco-labels guiding
consumer choice.
2000s
Wi-Fi-enabled “smart fridges”
with touchscreens, cameras,
and connectivity to
smartphones.
Inverter compressors for
quieter, more eﬃcient cooling.
LED lighting and advanced
insulation further cut energy
use.
2010s
Version: 19d8ced | © 05.10.2026 University of Southampton
31

## Slide 32
Systematic design provides a structured and methodical way to manage the complexity inherent in large,
multi-component systems.
It is both a mindset and a methodology, drawing from systems thinking, optimisation, and domain-speciﬁc
engineering practices.
By integrating stakeholder needs, technical constraints, and adaptive feedback, systematic design becomes
essential not just for building systems that work, but for building systems that can evolve.
SEAtS | 264726
Conclusion
Version: 19d8ced | © 05.10.2026 University of Southampton
32

## Slide 33
Dr Nawfal Al Hashimy
Lecturer in Cyber Physical Security
Universtity of Southampton | Faculty of Engineering and Physical
Sciences
Cyber Physical Systems Research Group
☎
+44 (0) 23 8059 6659
@ Nawfal@soton.ac.uk
Highﬁeld Campus, Building 53, Room 4049
Burgess Road, Southampton SO17 1BJ, UK
Thank you